## Slide 1
Reverse Engineering
Pump ECU Flash Protocol
How JSW Controls & Software decoded a proprietary CAN protocol, adapted it to our hardware, and eliminated all OEM tool dependency.
JSW Air Pump ✦ JSW Oil Pump ✦ PEAK PCAN Hardware ✦ Integrated into JSW FlashXpert V1.4
Controls & Software Department R&D — JSW Greentech Limited | 2025
JSW FlashXpert V1.4

## Slide 2
The Problem — OEM Tool Dependency
Before reverse engineering: no control, no visibility, no integration
OEM Tool Blockers
✗ candebug.exe — closed binary, no source code
✗ Requires USBCAN hardware (not our PEAK adapters)
✗ GUI-only — no automation or scripting possible
✗ OEM presence required for every firmware update
✗ Zero error details — pass/fail only
✗ Cannot integrate with our existing JSW FlashXpert tool
Business Risk
✗ Single point of failure — if OEM tool breaks, no flash
✗ Production line dependency on OEM availability
✗ Protocol fully unknown — cannot debug field failures
✗ No log, no traceability for flashed units
✗ Different workflow for pumps vs all other ECUs
✗ Cannot detect bad flash sectors proactively
Goal: Fully decode the protocol from CAN traffic alone → implement in Python → run on PEAK hardware we already own → ship as part of JSW FlashXpert → never need the OEM tool again.
Scope
✦ JSW Oil Pump (ECU addr 0x05) ✦ JSW Air Pump (ECU addr 0x06)
✦ Custom 8-byte CAN protocol over 29-bit extended IDs at 250 kbps
✦ Intel HEX firmware files | VER1, VER2, VER3 variants
JSW Greentech Limited — Controls & Software Department | CONFIDENTIAL
JSW FlashXpert V1.4

## Slide 3
Reverse Engineering Method — 4-Step Approach
No documentation, no source code — protocol decoded entirely from live CAN traffic
01
Passive CAN Capture
Connected PEAK PCAN-USB to the vehicle CAN bus Ran OEM tool to flash a known-good pump ECU Captured full timestamped CAN log during flash
→
02
Frame Identification
Filtered IDs 0x180005FF ↔ 0x1800FF05 Confirmed 0x1800FFFF as broadcast channel Identified 0x1800EEEE as NAK/error channel
→
03
Pattern Analysis
All frames exactly 8 bytes — consistent structure Byte[7] = XOR of bytes[0..6] → checksum rule Byte[0] cycles: 0x04→0x01→0x02→0x01→… per block
04
ACK Mechanism
ECU replies with the EXACT same 8 bytes Reply arrives on ECU ID (not tool ID) No echo within window = timeout → retry / fail
→
05
Firmware Mapping
Decoded address payload: 4B addr + 2B size Matched HEX file records to CAN data frames Verified 6 payload bytes per data frame
→
06
Validate & Replicate
Wrote Python script to replay captured sequence Compared byte-for-byte with OEM log Flashed ECU successfully — protocol confirmed ✓
JSW Greentech Limited — Controls & Software Department | CONFIDENTIAL
JSW FlashXpert V1.4

## Slide 4
Protocol Fully Decoded — 8-Byte Custom CAN Frame
Complete frame specification recovered from CAN traffic analysis
Frame layout: [ TYPE ][ P1 ][ P2 ][ P3 ][ P4 ][ P5 ][ P6 ][ XOR8 ] XOR8 = P0 XOR P1 XOR P2 XOR P3 XOR P4 XOR P5 XOR P6
0x00
Heartbeat / End-of-Block
Wakeup: 00 00 <hb_byte> 00 00 00 00 <XOR> End-of-block: 00 00 <block_id> … <XOR>
0x01
Data Frame (Toggle A)
Payload = P1..P6 = 6 bytes of firmware data Alternates with 0x02 for every 6-byte chunk
0x02
Data Frame (Toggle B)
Identical to 0x01 but TYPE byte = 0x02 Toggle ensures ECU detects duplicate/lost frames
0x03
Close Session
Sent after verify — closes flash session Payload carries CRC bytes from HEX file
0x04
Block Init / Erase
P1-P4 = full 32-bit address (big-endian) P5-P6 = block size in bytes (big-endian)
Broadcast Wakeup (live ECU): FF 02 <ecu_addr> 00 00 00 00 <XOR> → sent on 0x1800FFFF → ECU ACKs with FF 82 <ecu_addr> … then reboots to bootloader in 300 ms
JSW Greentech Limited — Controls & Software Department | CONFIDENTIAL
JSW FlashXpert V1.4

## Slide 5
CAN ID Map & Flash Sequence
All extended 29-bit IDs at 250 kbps | Echo-ACK model
CAN ID
Direction
Purpose
Example Frame
0x1800FFFF
Tool → All ECUs
Broadcast wakeup
FF 02 05 00 00 00 00 FD
0x180005FF
Tool → Oil Pump
Commands & data
04 00 3E 80 00 20 00 BC
0x1800FF05
Oil Pump → Tool
Echo-ACK (mirrors frame)
04 00 3E 80 00 20 00 BC
0x180006FF
Tool → Air Pump
Commands & data
00 00 07 00 00 00 00 07
0x1800FF06
Air Pump → Tool
Echo-ACK (mirrors frame)
00 00 07 00 00 00 00 07
0x1800EEEE
ECU → Tool
NAK / Error response
00 3E 80 00 04 00 00 00
COMPLETE FLASH SEQUENCE
1
Broadcast Wakeup
FF 02 05… on 0x1800FFFF
→
2
Heartbeat Loop
00 00 07… 60× @ 100ms
→
3
Block Init & Erase
04 <addr> <size>
→
4
Data Frames
01/02 toggle 6B each
→
5
End of Block
00 00 <id> …
→
6
Write CRC
04 on CRC address
→
7
Verify & Close
01 verify 03 close
JSW Greentech Limited — Controls & Software Department | CONFIDENTIAL
JSW FlashXpert V1.4

## Slide 6
Key Discovery — VER1 Stride Anomaly & OEM Block Parser
Why Oil Pump VER1 needed a special block-splitting algorithm
What Went Wrong with VER1
✗ Our first tool sent 5 sequential 16 KB blocks
✗ Flash appeared to complete — no errors reported
✗ ECU booted BUT firmware CRC mismatch on reboot
✗ ECU rejected firmware and stayed in bootloader
Root cause: OEM tool splits VER1 differently — 7 blocks
How We Found It
✦ Captured OEM tool CAN log for VER1 flash
✦ Compared 0x04 (block init) frame addresses
✦ OEM sends 7 block-init frames — we sent only 5
✦ Analysed VER1 Intel HEX file record addresses
✦ Discovered non-contiguous records at 2 locations
✦ Gap between records > half the record byte count
STRIDE ANOMALY DETECTION ALGORITHM
for each record in HEX file:
if (current_addr - prev_addr) > prev_byte_count / 2:
→ STRIDE ANOMALY → start new block here
if sector changes (addr // 0x2000 differs):
→ SECTOR BOUNDARY → start new block here
Block ID Assignment
block_id = (0x3F4000 − block_addr) ÷ 0x2000
Last block always gets block_id = 1
VER1 → 7 blocks: IDs 6, 5, 5, 4, 3, 2, 1
VER2/3 → 5 blocks: IDs 6, 5, 4, 3, 1 (no anomaly)
Result
✅ Auto-detection: parse HEX → detect anomalies → choose OEM parser OR sequential parser automatically
✅ VER1 now flashes correctly with exactly the same block structure as the OEM tool
✅ VER2 and VER3 use the simpler sequential path — no OEM parser needed
JSW Greentech Limited — Controls & Software Department | CONFIDENTIAL
JSW FlashXpert V1.4

## Slide 7
Addressing, Heartbeat Formula & Wakeup Modes
How the tool identifies the ECU and handles both live and cold-start scenarios
ECU Addressing
dev_id in CAN ID (low byte):
Oil Pump → 0x05
Air Pump → 0x06
Tool TX: 0x1800 00 <dev_id> FF
ECU RX: 0x1800 FF <dev_id> 00
Broadcast: 0x1800FFFF (shared)
Heartbeat Byte Formula
hb_byte = (BLOCK_ID_BASE − base_addr)
÷ ADDR_STEP + 1
BLOCK_ID_BASE = 0x003F4000
ADDR_STEP = 0x2000 (8 KB)
base 0x3E8000 → hb_byte = 0x07
base 0x3EA000 → hb_byte = 0x06
Auto-read from Intel HEX file ✓
Why It Matters
hb_byte tells ECU which
flash sectors to unlock
Wrong hb_byte →
ECU ignores heartbeat
→ flash never starts
OEM tool hardcoded it.
We compute it from HEX.
TWO WAKEUP MODES — HANDLED AUTOMATICALLY
Mode A — Live Running ECU
ECU is powered and running application firmware
1. Send broadcast: FF 02 <ecu_addr> 00… on 0x1800FFFF
2. ECU ACKs with: FF 82 <ecu_addr> 00… on ecu_id
3. ECU reboots into bootloader (300 ms)
4. Start heartbeat loop — ECU responds quickly
5. Flash proceeds normally
Mode B — Cold Start / Already in Bootloader
ECU is powered off or already in bootloader
1. Send broadcast (no ACK expected — ECU not running)
2. Start heartbeat loop — 60 attempts × 100 ms = 6 s
3. User powers on ECU during heartbeat window
4. ECU boots into bootloader, sees heartbeat, responds
5. Flash proceeds normally
JSW Greentech Limited — Controls & Software Department | CONFIDENTIAL
JSW FlashXpert V1.4

## Slide 8
Integration into JSW FlashXpert V1.4 — Common Tool
Pump flashing added as a new tab in the same tool used for VCU, MCU, and all other ECUs
Common Tool Architecture
JSW FlashXpert V1.4 (jsw_gui.py + flashing_logic.py)
├─ CANBusWrapper PEAK / Vector / Kvaser
├─ FlashingLogic VCU / MCU (UDS / ISO-TP)
├─ PumpFlashingLogic Oil Pump + Air Pump ← NEW
│ ├─ _pump_load_hex() HEX parser
│ ├─ _pump_build_oem_blocks() VER1 stride fix
│ └─ _pump_build_blocks_sequential()
└─ FOTAFlashingLogic Phase 2 VCU FOTA ← NEW
What Was Eliminated
✅ candebug.exe — no longer needed
✅ USBCAN hardware — no longer needed
✅ OEM engineer dependency — gone
✅ Separate workflow for pumps — gone
✅ Unknown error codes — now fully logged
✅ Manual block counting — auto-detected
✅ Hardcoded heartbeat byte — computed from HEX
✅ No traceability — full timestamped log
✅ Single EXE — no Python needed on target PC
Hardware
PEAK PCAN-USB
(already in field)
PCANBasic.dll
direct integration
No additional
hardware purchase
Validated On Vehicle
✅ Oil Pump VER1 — 7 OEM blocks
✅ Oil Pump VER2 — 5 seq blocks
✅ Oil Pump VER3 — 5 seq blocks
✅ Air Pump — live ECU wakeup
✅ Bad sector ECU diagnosed
(1798ms vs 860ms erase time)
✅ Broadcast wakeup confirmed
Key Numbers
8 bytes — frame size
6 bytes — payload per frame
250 kbps — CAN bitrate
8 KB — sector / addr step
16 KB — max block size
0x2000 — ADDR_STEP
0x3F4000 — BLOCK_ID_BASE
JSW Greentech Limited — Controls & Software Department | CONFIDENTIAL
JSW FlashXpert V1.4

## Slide 9
Full Protocol Ownership.
Zero OEM Dependency.
We reverse-engineered a proprietary CAN flash protocol from captured traffic alone, implemented it in Python using PEAK hardware we already own, auto-detect all firmware variants, handle live and cold-start ECUs — integrated directly into JSW FlashXpert V1.4 as a new tab alongside VCU/MCU flashing. One tool. All ECUs. No OEM tools.
Controls & Software Department — R&D, JSW Greentech Limited | 2025
JSW FlashXpert V1.4
JSW Greentech Limited — Controls & Software Department | CONFIDENTIAL
JSW FlashXpert V1.4