## Slide 1
JSW FlashXpert
V2.0 — Tool Upgrade Presentation
New Capabilities Added:
✦ Oil Pump ECU Flashing ✦ Air Pump ECU Flashing ✦ Phase 2 — VCU FOTA Flashing
Controls & Software Department R&D — JSW Greentech Limited
2025

## Slide 2
Agenda
What this presentation covers
01
Tool Overview
Original JSW FlashXpert capabilities
02
Oil Pump Flashing
Custom CAN protocol — OEM block parser
03
Air Pump Flashing
Same protocol, different ECU address
04
Phase 2 — VCU FOTA
UDS over ISO-TP, 10-step sequence
05
Live Pump Monitor
Real-time CAN data dashboard
06
Architecture & Key Facts
Protocol summary, CAN IDs, tech stack
JSW Greentech Limited — Controls & Software Department | CONFIDENTIAL
JSW FlashXpert V2.0

## Slide 3
JSW FlashXpert — Original Tool
Capabilities before this upgrade
Original Supported Controllers
• JSW EVCU (Electric Vehicle Control Unit)
• JSW MCU (Motor Control Unit)
• JSW DCDC (DC-DC Converter)
Flash Protocol (UDS)
• Custom 8-byte CAN frames over extended IDs
• Programming session → Erase → Download → Verify → Reset
• CRC32 post-flash handshake
• Ignition OFF → ON procedure for all controllers
Other Features
• Read firmware version (JSW MCU & EVCU)
• Progress sidebar with 6-step visual tracker
• Save / clear flash log
• Domain-join security check
Hardware Support
• PEAK PCAN (PCANBasic.dll)
• Vector CANalyzer interface
• Kvaser CAN adapter
• Fixed 250 kbps for all controllers
JSW Greentech Limited — Controls & Software Department | CONFIDENTIAL
JSW FlashXpert V2.0

## Slide 4
V2.0 — What's New at a Glance
Three major features added to JSW FlashXpert
Oil Pump ECU Flashing
✓ Custom 8-byte CAN protocol
✓ OEM stride-anomaly block parser
✓ Broadcast wakeup (live ECU)
✓ Power OFF → ON procedure
✓ dev_id = 0x05 | 250 kbps
Air Pump ECU Flashing
✓ Same custom CAN protocol
✓ Sequential block builder
✓ Broadcast wakeup support
✓ Power OFF → ON procedure
✓ dev_id = 0x06 | 250 kbps
Phase 2 VCU FOTA Flash
✓ UDS over ISO-TP (can-isotp)
✓ 10-step UDS sequence
✓ SecurityAccess.dll key derive
✓ OTA binary with OtaPlainHdr
✓ TX 0x7E0 / RX 0x7E8
JSW Greentech Limited — Controls & Software Department | CONFIDENTIAL
JSW FlashXpert V2.0

## Slide 5
Oil Pump ECU Flashing
JSW Oil Pump — dev_id 0x05 | Custom 8-byte CAN protocol
CAN IDs
• Broadcast : 0x1800FFFF
• Tool → ECU : 0x180005FF
• ECU → Tool : 0x1800FF05
• NAK : 0x1800EEEE
Flash Sequence
• 1. Broadcast wakeup (FF 02 05 …) — reboots live ECU
• 2. Heartbeat until ECU responds (up to 60 × 100 ms)
• 3. Block init + erase per block (0x04 frame)
• 4. Data frames toggle 0x01 / 0x02 (6 bytes payload each)
• 5. End-of-block frame (0x00 + block_id)
• 6. Program CRC address (0x04 on CRC addr)
• 7. Verify CRC (0x01 frame)
• 8. Close session (0x03 frame)
Firmware Versions
• VER1: stride anomalies → OEM block parser (7 blocks)
• VER2 / VER3: sequential → 5 blocks at 0x3E8000
• Stride anomaly detection: gap > prev_bc ÷ 2
• Block IDs auto-computed from BLOCK_ID_BASE
Frame Format
• 8 bytes: [TYPE][P1][P2][P3][P4][P5][P6][XOR8]
• XOR8 = XOR of first 7 bytes
• ACK = ECU echoes exact frame on ECU ID
• Payload = 6 bytes of firmware data per frame
JSW Greentech Limited — Controls & Software Department | CONFIDENTIAL
JSW FlashXpert V2.0

## Slide 6
Air Pump ECU Flashing
JSW Air Pump — dev_id 0x06 | Same protocol, different address
CAN IDs
• Broadcast : 0x1800FFFF (shared)
• Tool → ECU : 0x180006FF
• ECU → Tool : 0x1800FF06
• NAK : 0x1800EEEE (shared)
Key Differences vs Oil Pump
• ECU address byte 0x06 (Oil Pump = 0x05)
• No stride anomalies — always sequential blocks
• Heartbeat byte auto-computed from hex base address
• Same 8-byte frame format, same ACK mechanism
• Same Power OFF → ON procedure in GUI
Heartbeat Byte Formula
• hb_byte = (BLOCK_ID_BASE − base_addr) ÷ 0x2000 + 1
• BLOCK_ID_BASE = 0x003F4000
• Example: base 0x3E8000 → hb_byte = 0x07
• Example: base 0x3EA000 → hb_byte = 0x06
• Auto-detected from Intel HEX file — no manual config
GUI Flow (Both Pumps)
• 1. Select pump type (Air / Oil)
• 2. Select CAN hardware + browse HEX file
• 3. Click Start Flashing
• 4. Dialog: TURN OFF power → click OK
• 5. Dialog: TURN ON power → flashing starts automatically
• 6. Progress sidebar turns green step by step
JSW Greentech Limited — Controls & Software Department | CONFIDENTIAL
JSW FlashXpert V2.0

## Slide 7
Phase 2 — VCU FOTA Flashing
S32K144 ECU | UDS over ISO-TP | SecurityAccess.dll
01
Diag Session
0x10 0x02 Catch bootloader
→
02
Security Access
0x27 01 seed 0x27 02 key
→
03
Erase
0x31 01 FF 00 App slot
→
04
Download
0x34 Request 0x36 Transfer
→
05
Verify
0x37 Exit 0x31 01 FF 01 CRC
→
06
ECU Reset
0x2E F1 5B FP 0x11 01 Reset
OTA Binary Format (OtaPlainHdr)
• Magic : 0xB00710AD (4 bytes)
• Model ID : 2 bytes (e.g. 0x0001 = 9M Bus)
• Version : 3 bytes (major.minor.patch)
• Reserved : 3 bytes
• Comp Size : 4 bytes (compressed payload size)
• Nonce : 12 bytes (encryption nonce)
• Payload : encrypted + compressed firmware
Security & Infrastructure
• SecurityAccess.dll — key derivation (ComputeKey)
• ISO-TP framing via can-isotp library
• CAN IDs: TX 0x7E0 / RX 0x7E8 (standard 11-bit)
• 0x78 NRC: ECU busy → auto-extend timeout to 5 min
• Separate tab (Phase 2) in GUI — different workflow
• Coloured log: green=OK red=error orange=warn
JSW Greentech Limited — Controls & Software Department | CONFIDENTIAL
JSW FlashXpert V2.0

## Slide 8
Bonus: Live Pump CAN Monitor
pump_monitor_gui.py — Replicates OEM candebug.exe tool
What It Shows (Oil Pump)
• Bus Voltage • Output Voltage • Output Current
• Set Frequency • Output Frequency • RPM
• Controller Temperature • Motor Temperature
• Run Enable • CAN Enable • Hardwire Enable
• Fault Code (row turns RED when non-zero)
• Stator R • D/Q Inductance • Back-EMF • PID gains
Monitor CAN IDs (from OEM tool)
• 0x4181 → Bus V, Output V, Current
• 0x4182 → Set Freq, Output Freq, RPM
• 0x4183 → Ctrl Temp, Motor Temp, Enable, Fault
• 0x4184 → CAN/Hardwire Enable flags
• 0x5010 → Motor parameters (R, L, EMF)
• 0x5011 → PID gains (DKp, DKi, QKp, QKi)
• Each frame = 4 × uint16 big-endian values
GUI Features
• Active CAN IDs light up GREEN when receiving frames
• CAN ID turns grey if silent > 1 second
• PEAK channel selector: PCAN_USBBUS1 / 2 / 3
• Frame counter displayed in real time
• Status bar shows interface + bitrate
Source: OEM Tool Analysis
• Reverse-engineered from candebug.exe config XMLs
• dcac_oil_config.xml • dcac_gas_config.xml
• dev_id 0x05 = Oil Pump • 0x06 = Air Pump
• BaudRate=3 → 250 kbps confirmed
JSW Greentech Limited — Controls & Software Department | CONFIDENTIAL
JSW FlashXpert V2.0

## Slide 9
Architecture & CAN ID Reference
All controllers supported by JSW FlashXpert V2.0
Controller
Protocol
Tool → ECU ID
ECU → Tool ID
Bitrate
Flash File
JSW EVCU
Custom UDS
0x0B00D0D9 (ext)
0x0B00D9D0 (ext)
250 kbps
.hex / .bin
JSW MCU
Custom UDS
0x0B00D0D9 (ext)
0x0B00D9D0 (ext)
250 kbps
.hex / .bin
JSW DCDC
Custom UDS
0x0B00D0D9 (ext)
0x0B00D9D0 (ext)
250 kbps
.hex / .bin
JSW Oil Pump
Custom 8-byte
0x180005FF (ext)
0x1800FF05 (ext)
250 kbps
Intel HEX
JSW Air Pump
Custom 8-byte
0x180006FF (ext)
0x1800FF06 (ext)
250 kbps
Intel HEX
VCU FOTA
UDS / ISO-TP
0x7E0 (std 11bit)
0x7E8 (std 11bit)
250 kbps
OTA .bin
OIL PUMP
AIR PUMP
VCU FOTA
EXISTING
Software Architecture
• flashing_logic.py — all protocol logic classes
• ├─ CANBusWrapper (PEAK / Vector / Kvaser)
• ├─ FlashingLogic (UDS, existing controllers)
• ├─ PumpFlashingLogic (Oil + Air Pump)
• └─ FOTAFlashingLogic (VCU FOTA, ISO-TP)
• jsw_gui.py — Phase 1 + Phase 2 tabbed GUI
• pump_monitor_gui.py — live CAN data monitor
JSW Greentech Limited — Controls & Software Department | CONFIDENTIAL
JSW FlashXpert V2.0

## Slide 10
Summary — JSW FlashXpert V2.0
Single tool for all JSW powertrain ECU flashing needs
Oil + Air Pump
✓ Both pump types in one tool
✓ Live ECU broadcast wakeup
✓ OEM-compatible block parser
✓ No separate OEM tool needed
VCU FOTA
✓ Full 10-step UDS sequence
✓ Separate Phase 2 tab
✓ OTA binary + DLL workflow
✓ Up to 5 min transfer exit
Pump Monitor
✓ Live CAN data dashboard
✓ RPM, voltage, temp, faults
✓ OEM-equivalent monitoring
✓ PEAK hardware support
Tool Quality
✓ Single .exe deployment
✓ Domain-join security check
✓ Coloured step-by-step sidebar
✓ Elapsed time + save log
JSW Greentech Limited — Controls & Software Department | CONFIDENTIAL
JSW FlashXpert V2.0

## Slide 11
Thank You
JSW FlashXpert V2.0 is ready for deployment.
For queries contact the Controls & Software Department, R&D — JSW Greentech Limited